NOTIFICATION

The following notification is being circulated in accordance with Article 10.6

| 1. | Notifying Member: New Zealand If applicable, name of local government involved (Article 3.2 and 7.2): |
| --- | --- |
| 2. | Agency responsible: Ministry of Business, Innovation & Employment P.O. Box: 10729 Wellington, New Zealand Phone: +64-4-9010 8603 Email: laurie.boyce@mbie.govt.nz; Web: http://www.mbie.govt.nz Name and address (including telephone and fax numbers, email and website addresses, if available) of agency or authority designated to handle comments regarding the notification shall be indicated if different from above: Energy Efficiency and Conservation Authority P.O. Box: 388 Wellington, New Zealand Phone: +64-4-470 2200 Email: laura.christen@eeca.govt.nz Web: http://www.eeca.govt.nz |
| 3. | Notified under Article 2.9.2 [ X ], 2.10.1 [ ], 5.6.2 [ ], 5.7.1 [ ], other: |
| 4. | Products covered (HS or CCCN where applicable, otherwise national tariff heading. ICS numbers may be provided in addition, where applicable): Household refrigerators and freezers Refrigerators, freezers and other refrigerating or freezing equipment, electric or other; heat pumps other than air conditioning machines of heading 84.15. (HS 8418). Domestic refrigerating appliances (ICS 97.040.30). |
| 5. | Title, number of pages and language(s) of the notified document: Proposed changes to regulatory requirements for household refrigerators and freezers can be found in the Equipment Energy Efficiency (E3) Decision Regulation Impact Statement - Household Refrigerators and Freezers (November 2017, 84 pages) available for download at: http://www.energyrating.gov.au/news/decision-regulation-impact-statement-household-refrigerators-and-freezers |
| 6. | Description of content: The E3 Decision Regulation Impact Statement - Household Refrigerators and Freezers presents proposed changes to regulatory requirements for household refrigerators and freezers offered for sale in New Zealand and Australia. The key changes are outlined below. Adoption of an international test method to replace local testing requirements: Parts 1, 2 and 3 of the International Electrotechnical Committee test standards (IEC 62552:2015) will be directly adopted into a joint Australia/New Zealand Standard, in three parts as follows: AS/NZS IEC 62552.1 Household refrigerating appliances - Characteristics and test methods - Part 1: General requirements AS/NZS IEC 62552.2 Household refrigerating appliances - Characteristics and test methods - Part 2: Performance requirements AS/NZS IEC 62552.3 Household refrigerating appliances - Characteristics and test methods - Part 3: Energy consumption and volume The Australia/New Zealand Standard AS/NZS IEC 62552 Parts 1, 2 and 3 will then be incorporated into the Energy Efficiency (Energy Using Products) Regulations 2002 in New Zealand (subject to Cabinet approval) and the equivalent regulation in Australia. The Australia/New Zealand Standard AS/NZS IEC 62552 Parts 1, 2 and 3 is expected to be published by mid February 2018. It will replace the Australia/New Zealand test standard AS/NZS 4474.1:2007 Performance of household electrical appliances - Refrigerating appliances - Energy consumption and performance. This will be withdrawn from regulation. The proposed test parameters are summarised in Attachment G (page 76) of E3 Decision Regulation Impact Statement. Update minimum energy performance standards (MEPS) MEPS requirements will be updated (subject to Cabinet approval) to significantly lower the maximum allowable energy consumption of refrigerators and freezers. A new version of Australia New Zealand standard AS/NZS 4474 will adopt MEPS levels equivalent to those adopted in the US on 15 September 2014, and will supersede AS/NZS 4474.2 Performance of household electrical appliances - Refrigerating appliances - Energy labelling and minimum energy performance standard requirements. The MEPS levels that will apply are set out in Attachment F (page 75) of the E3 Decision Regulation Impact Statement. The proposed performance parameters for MEPS are set out in Attachment G (page 76) - see Table 37: Generally agreed performance parameters (Option C) on page 77. The revised Australia/New Zealand Standard AS/NZS 4474 is not due to be published until November 2018 but a public comment draft will be available for viewing in April 2018. An addendum to this notification will be issued when the public comment draft becomes available. Modify the Energy Rating Label algorithm The Energy Rating Label algorithm is not being re-graded but it will be adjusted to maintain continuity of energy ratings as Australia and New Zealand transition to a new test method and MEPS levels. The modifications to the Energy Rating Label algorithm are intended to: maintain comparability between products registered against the outgoing test method and new products registered against AS/NZS IEC 62552 as far as possible, ensure that currently registered products able to comply with the new MEPS levels will have comparable ERL ratings when registered using the test standard AS/NZS IEC 62552, and will not be penalised with a lower star rating ensure that ratings remain spread out across the rating scale and that the lower rating bands continue to be used (these lower rating bands would otherwise be largely emptied due to the introduction of a higher MEPS level) reward more efficient products with upwards adjustments to their star ratings move the labelled energy to a value that more closely represents typical product use, which will encourage suppliers to optimise energy consumption and performance under normal use conditions. More information on the Energy Rating Label algorithm modifications can be found in Section 4 of the E3 Decision Regulation Impact Statement - Household Refrigerators and Freezers (see subsection 4.3.5 ERL algorithm parameters, on page 28), and in the E3 report Household Refrigeration Appliances: New Star Rating Algorithm Proposal for the IEC Test Method (June 2015), available at: http://energyrating.gov.au/document/report-household-refrigeration-appliances-new-star-rating-algorithm-proposal-iec-test. |
| 7. | Objective and rationale, including the nature of urgent problems where applicable: The proposed measures will ensure the ongoing effectiveness of minimum energy performance standards (MEPS) and the Energy Rating Label in New Zealand. MEPS and labelling will continue to function as a means to improve the energy performance of products and provide better information on their energy use. This makes it easier for businesses and households to invest in energy efficient products and reduce their energy costs. At a national level, this will result in lower household electricity demand and fewer greenhouse gas emissions than would otherwise occur. The proposed measures therefore contribute to the Government’s priorities “Efficient use of energy” under the New Zealand Energy Strategy 2011-2021 and “innovative and efficient use of electricity” under the New Zealand Energy Efficiency and Conservation Strategy (2017-2022), as well as the target to reduce greenhouse gas emissions in New Zealand to 30 percent below 2005 levels by 2030. Adopting these measures will also maintain alignment of regulation between Australia and New Zealand. This helps uphold the two countries’ commitments under the Australia-New Zealand Closer Economic Relations Agreement (ANZCERTA) and the trans-Tasman Mututal Recognition Arrangement (TTMRA). The migration from a local to an international test method promotes closer alignment with international standards and reduces suppliers’ compliance costs. |
| 8. | Relevant documents: The E3 Decision Regulation Impact Statement - Household Refrigerators and Freezers, (November 2017) is available for download at: http://www.energyrating.gov.au/news/decision-regulation-impact-statement-household-refrigerators-and-freezers The E3 report Household Refrigeration Appliances: New Star Rating Algorithm Proposal for the IEC Test Method (June 2015), available at: http://energyrating.gov.au/document/report-household-refrigeration-appliances-new-star-rating-algorithm-proposal-iec-test The Energy Efficiency (Energy Using Products) Regulations 2002 (the Regulations) are available at: http://www.legislation.govt.nz. Once published, Australia New Zealand Standards will be available from the Standards New Zealand website at: https://www.standards.govt.nz/. |
| 9. | Proposed date of adoption: The proposed regulatory changes will be incorporated into New Zealand Regulation no earlier than 1 December 2018. Proposed date of entry into force: The proposed MEPS requirements for household refrigerators and freezers will come into force in New Zealand Regulation no earlier than January 2021. (This accommodates a two-year lead-in time negotiated with industry during consultation on this proposal.) |
| 10. | Final date for comments: 23 February 2018 |
| 11. | Texts available from: National enquiry point [ ] or address, telephone and fax numbers and email and website addresses, if available, of other body: Energy Efficiency and Conservation Authority P.O. Box: 388 Wellington, New Zealand Phone: +64-4-470 2200 Email: laura.christen@eeca.govt.nz Web: http://www.eeca.govt.nz, http://www.energyrating.gov.au http://www.energyrating.gov.au/news/decision-regulation-impact-statement-household-refrigerators-and-freezers http://energyrating.gov.au/document/report-household-refrigeration-appliances-new-star-rating-algorithm-proposal-iec-test |