NOTIFICATION

The following notification is being circulated in accordance with Article 10.6

| 1. | Notifying Member: Jamaica If applicable, name of local government involved (Article 3.2 and 7.2): |
| --- | --- |
| 2. | Agency responsible: Bureau of Standards Jamaica Name and address (including telephone and fax numbers, email and website addresses, if available) of agency or authority designated to handle comments regarding the notification shall be indicated if different from above: Regional and International Trade Branch 6 Winchester Road Kingston 10 Jamaica W.I. Email: tbtenquirypoint@bsj.org.jm Website: http://www.bsj.org.jm Tel.: 1 (876) 926-3140-5/618-1534/ 632-4275 Fax: 1 (876) 929-4736 |
| 3. | Notified under Article 2.9.2 [X], 2.10.1 [ ], 5.6.2 [ ], 5.7.1 [ ], other: |
| 4. | Products covered (HS or CCCN where applicable, otherwise national tariff heading. ICS numbers may be provided in addition, where applicable): Transportable gas containers, ICS 23.020.30; Fluid storage devices (ICS 23.020) |
| 5. | Title, number of pages and language(s) of the notified document: Standard Specification for Transportable gas cylinders – Fully wrapped composite cylinders (63 page(s), in English) |
| 6. | Description of content: This standard specifies minimum requirements for the materials, design, construction, prototype testing and routine manufacturing inspections of composite gas cylinders with a water capacity up to and including 450 l for compressed, liquefied and dissolved gases. |
| 7. | Objective and rationale, including the nature of urgent problems where applicable: This draft standard is a revision of and supersedes JS 322: 2012. It specifies the minimum requirements for the materials, design, construction, prototype testing and routine manufacturing inspections of fully wrapped composite gas cylinders with a water capacity up to and including 450 litres for compressed, liquefied and dissolved gases. This standard should also be applicable to cylinders that comprise a liner of metallic material (welded or seamless) or non-metallic material (or a mixture thereof), reinforced by a wound composite consisting of fibres of glass, carbon or aramid (or a mixture thereof) embedded in a matrix. The objective and rationale is that the standard is seven (7) years old and due for systematic revision. These composite cylinders will be offered for sale on the local market within the next few months. The revised standard is intended to be mandatory and aims to provide assurance that adequate health and safety protection exists for the intended users of the cylinders; Not specified |
| 8. | Relevant documents: A notice of the Standard Speciﬁcation for Composite cylinders, transportable gas containers will appear in The Jamaica Gazette Supplement - Proclamations, Rules and Regulations. The document will appear as a Jamaican Standard Specification, with mandatory status, and will be available for sale. |
| 9. | Proposed date of adoption: 12 November 2021 Proposed date of entry into force: 12 November 2021 |
| 10. | Final date for comments: 60 days from notification |
| 11. | Texts available from: National enquiry point [X] or address, telephone and fax numbers and email and website addresses, if available, of other body: The full text of the proposed technical regulation (mandatory standard) can be directly accessed on the website of the Bureau Standards Jamaica: http://www.bsj.org.jm tbtenquirypoint@bsj.org.jm |