NOTIFICATION

The following notification is being circulated in accordance with Article 10.6

| 1. | Notifying Member: Canada If applicable, name of local government involved (Article 3.2 and 7.2): |
| --- | --- |
| 2. | Agency responsible: Department of Transport Name and address (including telephone and fax numbers, email and website addresses, if available) of agency or authority designated to handle comments regarding the notification shall be indicated if different from above: Canada's Notification Authority and Enquiry Point Technical Barriers and Regulations Division Global Affairs Canada 111 Sussex Drive Ottawa, Ontario, K1A 0G2 Canada Telephone: (343)203-4273 Fax: (613)943-0346 Email: enquirypoint@international.gc.ca |
| 3. | Notified under Article 2.9.2 [X], 2.10.1 [ ], 5.6.2 [ ], 5.7.1 [ ], other: |
| 4. | Products covered (HS or CCCN where applicable, otherwise national tariff heading. ICS numbers may be provided in addition, where applicable): Motor vehicles; Road vehicles in general (ICS 43.020), Commercial vehicles (ICS 43.080) |
| 5. | Title, number of pages and language(s) of the notified document: Regulations Amending Certain Regulations Made under the Motor Vehicle Safety Act (Minimum Sound Requirements for Hybrid and Electric Vehicles), (16 pages, available in English and French) |
| 6. | Description of content: The proposed safety standard includes requirements to testable acoustic parameters when the vehicle is about to move or is moving at low speeds. These requirements would ensure that blind, visually impaired, and other pedestrians and pedal cyclists are able to detect and recognize nearby hybrid and electric vehicles. These specifications should allow the pedestrian to recognize that there is a vehicle present, where that vehicle is, and in what state it is operating, more precisely, if the vehicle is accelerating or decelerating, going forward or reversing. It is important to note that HEVs currently on the road in Canada voluntarily conform to either the U.S. or UN requirements. The goal would be to incorporate the two sets of requirements into a Canadian standard, allowing manufacturers to choose which requirement to adopt (i.e. either the U.S. or UN requirement), thereby codifying an already existing practice. |
| 7. | Objective and rationale, including the nature of urgent problems where applicable: The objective of this proposal is to introduce a requirement in Canadian regulations to require hybrid and electric light vehicles to meet minimum sound requirements at low speeds in order to maintain a minimum level of safety for pedestrians and pedal cyclists, including the blind and visually impaired. The minimum sound generated by hybrid and electric light vehicles would be comparable to the sound generated by conventionally powered vehicles; Other |
| 8. | Relevant documents: Canada Gazette, Part I, 24 April 2021, pages 1765-1780 (available in English and French) |
| 9. | Proposed date of adoption: On the date of publication in the Canada Gazette, Part II. Proposed date of entry into force: These Regulations would come into force on the day on which they are published in the Canada Gazette, Part II. |
| 10. | Final date for comments: 17 July 2021 |
| 11. | Texts available from: National enquiry point [X] or address, telephone and fax numbers and email and website addresses, if available, of other body: The electronic version of the regulatory text can be found at: https://canadagazette.gc.ca/rp-pr/p1/2021/2021-04-24/html/reg3-eng.html https://canadagazette.gc.ca/rp-pr/p1/2021/2021-04-24/html/reg3-fra.html |