NOTIFICATION

The following notification is being circulated in accordance with Article 10.6

| 1. | Notifying Member: Republic of Korea If applicable, name of local government involved (Article 3.2 and 7.2): |
| --- | --- |
| 2. | Agency responsible: Ministry of Land, Infrastructure and Transport (MOLIT) Name and address (including telephone and fax numbers, email and website addresses, if available) of agency or authority designated to handle comments regarding the notification shall be indicated if different from above: Motor Vehicles Policy Division Bureau of Motor Vehicles Policy Ministry of Land, Infrastructure and Transport 11, Doum-ro 6, Sejong city, 30103 Republic of Korea Tel.: (+82) 44-201-3850 Fax: (+82) 44-201-5584 E-mail: herdong1928@korea.kr Website: http://www.molit.go.kr |
| 3. | Notified under Article 2.9.2 [X], 2.10.1 [ ], 5.6.2 [ ], 5.7.1 [ ], other: |
| 4. | Products covered (HS or CCCN where applicable, otherwise national tariff heading. ICS numbers may be provided in addition, where applicable): Motor Vehicles; VEHICLES OTHER THAN RAILWAY OR TRAMWAY ROLLING STOCK, AND PARTS AND ACCESSORIES THEREOF (HS 87) |
| 5. | Title, number of pages and language(s) of the notified document: Revision of 'Rules on the Performance and Standards for Motor Vehicles and their Parts' (previously notified as 'Korean Safety and Performance Regulations for Motor Vehicles and Parts' on May 2020) (92 page(s), in Korean) |
| 6. | Description of content: The following amendments will be made to the Rules on the Performance and Standards for Motor Vehicles and their Parts. A. Draft Article 15-3 and 90-3 will require Advanced Emergency Braking System (AEBS) in passenger vehicles and trucks and special purpose vehicles with Gross Vehicle Mass (GVM) of 3.5 tons or less. Before this amendment, the AEBS requirement was applied only for buses and trucks and special purpose vehicles with GVM exceeding 3.5 tons. This requirement will be amended to be applied to passenger vehicles and trucks and special purpose vehicles with GVM of 3.5 tons or less. Also, the performance requirement for AEBS will be newly established. B. Draft Article 19 and 32 will improve the payload markings and the standards for goods-loading accommodation. The markings of the GVM and maximum payload of truck will be clarified; the specific gravity for dump truck and special purpose vehicle will be deleted so that manufacturers themselves can set the size of cargo box within the permitted range. C. Draft Article 38-4, 39, 40-2 and 44-2 will improve the standards for lamps. This amendment will clarify the number of reversing lamps and standards for end outline marker lamps installed on a vehicle, allow the installation of side marker lamps for a vehicle of which width does not exceed 6 m, ease the observing angle of rear position lamps of a vehicle on which side marker lamp is installed, and permit the installation of additional direction indicator lamps. D. Draft Article 91, 91-2, 91-3, 91-4, 102 and 102-3 will harmonize with the international standards for fuel system and collision test. The standards for fuel system will be reorganized by categories of fuel; fuel system safety in the case of rollover will be newly inserted; the collision standards for trucks with GVM of no more than 3.5 tons will be harmonized with international standards. E. Draft Table 5-30 will form the basis for installing a service door on the left side of a bus with a seating capacity of 16 or more. This amendment will lay the foundation for installing a service door on the left side of buses with a seating capacity of 16 or more passengers in case it is deemed that the service door on the left side has proper preventive measures against malfunction and operate safely. |
| 7. | Objective and rationale, including the nature of urgent problems where applicable: The reform is to resolve the problems found in the current system by requiring AEBS to be installed in passenger vehicles and trucks and special purpose vehicles with GVM of 3.5 tons or less, including a provision for installing a service door on the left side of a bus with a seating capacity of 16 or more, clarifying the markings on the back of a truck which indicates GVM and maximum payload, improving the standards for luggage compartment, amending the provisions of lamps to prevent traffic accidents caused by confusing lamps, and harmonizing the fuel system and collision standards for light duty vehicles with international standards.; Protection of human health or safety; Harmonization |
| 8. | Relevant documents: MOLIT Notice No. 2022-196 |
| 9. | Proposed date of adoption: December 2022 or later Proposed date of entry into force: January 2023 or later |
| 10. | Final date for comments: 60 days from notification |
| 11. | Texts available from: National enquiry point [X] or address, telephone and fax numbers and email and website addresses, if available, of other body: Korea WTO TBT Enquiry Point Technical Barriers to Trade (TBT) Division Korean Agency for Technology and Standards (KATS) 93 Isu-ro Maengdong-myeon Eumseong-gun Chungchungbuk-do 27737 +(82) 43 870 5521 +(82) 43 870 5682 (Fax) tbt@korea.kr http://www.knowtbt.kr https://members.wto.org/crnattachments/2022/TBT/KOR/22_1738_00_x.pdf https://members.wto.org/crnattachments/2022/TBT/KOR/22_1738_01_x.pdf |