| World Trade Organization |  |
| --- | --- |
|  | G/TBT/N/CAN/7 20 June 2001 |
|  | (01-3084) |
| Committee on Technical Barriers to Trade | Original: English/ French |

NOTIFICATION

The following notification is being circulated in accordance with Article 10.6.

| 1. | Member to Agreement notifying: CANADA If applicable, name of local government involved (Articles 3.2 and 7.2): |
| --- | --- |
| 2. | Agency responsible: Department of Transport Name and address (including telephone and fax numbers, e-mail and web-site addresses, if available) of agency or authority designated to handle comments regarding the notification shall be indicated if different from above: Canadian Enquiry Point, 200-270 Albert Street, Ottawa, Ontario, Canada, K1P 6N7 Tel.: +1 613 238-3222, ext. 491, Fax.: +1 613 569-7808, E-mail: idelage@scc.ca |
| 3. | Notified under Article 2.9.2 [X], 2.10.1 [ ], 5.6.2 [ ], 5.7.1 [ ], other: |
| 4. | Products covered (HS or CCCN where applicable, otherwise national tariff heading. ICS numbers may be provided in addition, where applicable): Electric vehicles (ICS 43.120) |
| 5. | Title, number of pages and language(s) of the notified document: Proposed Amendment to the Motor Vehicle Safety Regulations (Electrolyte Spillage and Electrical Shock Protection) (pages 1865-1870; English and French) |
| 6. | Description of content: This amendment establishes a new Canada Motor Vehicle Safety Standard (CMVSS) 305, “Electrolyte spillage and electrical shock protection” addressing safety issues exclusive to electric vehicles. It applies to all passenger cars, and to multipurpose passenger vehicles, trucks and buses with a Gross Vehicle Weight Rating (GVWR) of 4 536 kg or less, that have a propulsion power source greater than 48 volts and can attain a speed in 1.6 km of more than 40 km/h on a paved level surface. This amendment will not apply to low-speed vehicles. This new safety standard will address the specific safety concerns surrounding the introduction of electric vehicles and hybrid-electric vehicles into Canada. Specifically, this amendment will put in place a series of crash tests which will establish the capability of the vehicle to protect the occupants from hazards related to electric shock, the spillage of electrolyte from the batteries, and the potential injury arising from the battery assembly entering the passenger compartment. |
| 7. | Objective and rationale, including the nature of urgent problems where applicable: To harmonize Canadian requirements to those of the United States. |
| 8. | Relevant documents: Canada Gazette, Part I, 2 June 2001 |
| 9. | Proposed date of adoption: Proposed date of entry into force: | ( | Not stated |
| 10. | Final date for comments: 1 August 2001 |
| 11. | Texts available from: National enquiry point [X] or address, telephone and fax numbers, e-mail and web-site addresses, if available of the other body: The electronic version of the Canada Gazette Part I can be downloaded at: http://canada.gc.ca/gazette/part1/pdf/g1-13522.pdf |